## Slide 1: Data Representation
Real Numbers

## Slide 2: Real Numbers
Contain both whole and fractional components
Require separation of components to be represented within computer circuitry
  Fixed radix point (simple)
  Floating point notation (complex)

## Slide 3
Fixed Point Notation
Fixed
Point !

## Slide 4: Fractional Numbers
Number |  | 1000 | 100 | 10 | 1 | Radix Point | 10th (.1) | 100th (.01) | 1000th (.001)
 | ± | 103 | 102 | 101 | 100 | . | 10-1 | 10-2 | 10-3
8172.469 |  |  |  |  |  |  |  |  | 
Number |  | 8 | 4 | 2 | 1 | Radix Point | 1/2 (.5) | 1/4 (.25) | 1/8 (.125)
 | ± | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3
11.625 |  |  |  |  |  |  |  |  | 
Decimal
Binary
Sign
bit
0 | 1 | 0 | 1 | 1 | . | 1 | 0 | 1
Let’s Solve this
8 | 1 | 7 | 2 | . | 4 | 9 | 6

## Slide 5: Solve these
Number |  | 16 | 8 | 4 | 2 | 1 | 1/2 (.5) | 1/4 (.25) | 1/8 (.125) | 1/16 (.0625) | 1/32 (.03125)
 | ± | 24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5
5.75 |  |  |  |  |  |  |  |  |  |  | 
-28.5 |  |  |  |  |  |  |  |  |  |  | 
12.625 |  |  |  |  |  |  |  |  |  |  | 
-5.9 |  |  |  |  |  |  |  |  |  |  | 
Solve the following:
Radix Point

## Slide 6: Solve it (solved)
Number |  | 16 | 8 | 4 | 2 | 1 | 1/2 (.5) | 1/4 (.25) | 1/8 (.125) | 1/16 (.0625) | 1/32 (.03125) | 1/64 (.015625) | 1/128 (.0078125)
 | ± | 24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6 | 2-7
5.75 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
-28.5 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
12.625 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
-5.9 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1
Solve the following:
Radix Point
What happened here?

## Slide 7: !Associative
Real numbers are not associative
  (a + b) + c != a + (b + c)
(a + b) + c | Equal? | a + (b + c)
(3.6 + 4.3) + 5.9 |  | 3.6 + (4.3+ 5.9)
13.8 |  | 13.799999999999999
Example:

## Slide 8: More 2C Math

## Slide 9: Solve the following: (show work)
13
- 16
11
- 2
-10
- (-5)
14
- 10

## Slide 10: Floating Point Notation
Similar to scientific notation, except that 2 is the base
  value = mantissa x 2exponent [1.# x 2n]
Less accurate and more difficult to process than two’s complement format
Trades numeric accuracy for range
  Value can have many digits of precision for large or small magnitudes, but not both simultaneously

## Slide 11: Floating Point Notation (8 bit)
Sign bit (s)
  0 = positive; 1 = negative
Exponent (e)
  Stored in Excess notation
  -1 for special case values
Mantissa (m)
  AKA: significand
________
Sign
bit
Exponent
Stored in Excess Notation
Mantissa
(-1)(s) x 1.{m} x 2(e – 3)
2(n-1)-1

## Slide 12
________
Sign
bit
Exponent
Mantissa
5
To Binary
101
101.0 = 101.0 x 20
101.0 x 20
0
1
0
0
0
1
1
0
= 101.0
= 1.01 x 22
Create a floating point number
To Excess
Notation
2(3-1)-1= 3
3 +2 = 5
6 => 101
1
Hidden
Bit
Format needed:
1.# x 2n
Set Sign
1.
Convert
2.
Rewrite
3.
Normalize
4.

## Slide 13
________
Sign
bit
Exponent
Mantissa
/2=2.5 x 21
Format needed:
1.# x 2n
Floating Points - Another approach
Doesn’t match format; do again
2.5/2=1.25 x 22
1
Matches; stop
To Excess
Notation
2(3-1)-1= 3
3 +2 = 5
5 => 101
Find Exponent
Find Mantissa
2.
3.
4.
Hidden Bit
5
0
1
1
Set Sign
1.
0

## Slide 14
________
Sign
bit
Exponent
Mantissa
/2=2.5 x 21
0
1
0
0
0
1
1
Floating Points - Another approach
2.5/2=1.25 x 22
1
0.25
Find Exponent
Find Mantissa
2.
3.
4.
>= 1 ?
Hidden Bit
0.5 x 2 = 1.0
>= 1 ?
0 x 2 = 0
5
x 2 = .5
Set Sign
1.
0

## Slide 15: 32 bit Format (Single)
Sign
bit
Exponent
Mantissa
1 bit
8 bits
23 bits
________________________________
11000001010010100111000001000101
-12.65241

## Slide 16: 64 bit Format (Double)
_________________________
_____________
_____________
_____________
Sign
bit
Exponent
Mantissa
1 bit
11 bit
52 bit
0100000000101001010011100000100010101110111110110010101010101110
12.65241

## Slide 17: Calculate (32 bit)
Number | Sign bit | Exponent | Mantissa
-12.625 |  |  | 
0.125 |  |  | 
-15.70 |  |  | 

## Slide 18: Calculate (32 bit) - Solved
Number | Sign bit | Exponent | Mantissa
-12.625 | 1 | 10000010 | 10010100000000000000000
0.125 | 0 | 01111100 | 00000000000000000000000
-15.70 | 1 | 10000010 | 11110110011001100110011

## Slide 19: Range, Overflow, and Underflow
Range
  Limited by number of bits in a floating point string and formats of mantissa and exponent fields
Overflow
  Can occur within the exponent
Underflow
  Occurs when absolute value of a negative exponent is too large to fit within allocated bits

## Slide 20: Precision and Truncation
Precision
  Accuracy is reduced as the number of digits available to store mantissa is reduced
Truncation
  Stores numeric value in the mantissa until available bits are consumed; discards remaining bits
  Causes an error or approximation which can magnify
  Programmers avoid by using integer types or Binary Coded Decimal

## Slide 21: To Infinity and Beyond
Interpretation | Sign bit | Exponent | Mantissa
Infinity | 0 | 11111111 | 00000000000000000000000
Negative Infinity | 1 | 11111111 | 00000000000000000000000
Not a Number (NaN) | 0 /1 | 11111111 | Any bits except all 0s
Denormalized Number | 0/1 | 00000000 | Any bits except all 0s